## Slide 1: CSCI 1101 Introduction to Computer Science
Introduction to Boolean Algebra and
Logic Circuits

## Slide 2: Circuits and Boolean Algebra
Computers are constructed from logic circuits
  Logic circuits perform operations on digital signals
  Usually implemented as circuits where signal values are restricted to a few values (e.g., binary circuits)
But first, a short intro to Boolean algebra

## Slide 3: Binary Circuits
Circuit with 2 possible states, open (x = 0) or closed (x = 1), where x is the input variable that controls the switch

## Slide 4: Boolean Algebra
Named for George Boole, who in 1849 introduced a scheme for describing in algebra the processes involved in logical reasoning
In 1930’s, Claude Shannon showed that Boolean algebra provided a means of describing circuits built with switches
Provides foundation for much of modern technology

## Slide 5: Fundamental Operations
Boolean algebra works with variables that can have only 2 values – true or false (1 or 0, respectively)
The fundamental operations of Boolean algebra are AND, OR, and NOT

## Slide 6: NOT Operation
NOT takes one variable/argument/input
NOT is true if the input variable is false
  NOT (true) = false
  NOT (false) = true
  We’ll see another way to represent this in a minute

## Slide 7: AND and OR Operations
An AND function of variables x1, x2, …, xn has the value 1 only if all n variables are equal to 1.
  AND is like multiplication
An OR function of variables x1, x2, …, xn has the value 1 if at least one, or more, of the n variables are equal to 1
  OR is like addition

## Slide 8: Truth Tables
Used to define logic operations
Truth table for AND and OR operations with 2 inputs, x1 and x2

## Slide 9: Extending AND and OR
AND and OR can be extended to n variables
Truth table for AND and OR operations with 3 inputs
What would the truth table for NOT look like?

## Slide 10: Axioms of Boolean Algebra
Boolean algebra is based on set of rules that are derived from a small number of basic assumptions – axioms
Basic assumption: Boolean algebra, B, involves elements that take on one of two values, 0 and 1.
The following axioms are assumed to be true…

## Slide 11: Axioms of Boolean Algebra

## Slide 12: Single Variable Rules (Theorems)
From the axioms, we define rules (theorems) for dealing with single variables
We can prove by perfect induction (substitute x = 0 and x = 1 in each expression and use axioms)

## Slide 13: Principle of Duality in Boolean Algebra
Given a logic expression, we get its dual by replacing all + with (and vice versa) and by replacing 0s with 1s and 1s with 0s.
The dual of any true statement, axiom or theorem, in Boolean algebra is also a true statement
This means that at least 2 different ways exist to express every logic function

## Slide 14: Two- and Three- Variable Properties
We often need to deal with a number of variables
Define some 2- and 3-variable identities
Give the dual of each identity
Often referred to as properties
If x, y, and z are variables in B, the following properties hold…

## Slide 15: Properties

## Slide 16: Properties

## Slide 17: Properties
We can prove by perfect induction (truth tables), algebraic manipulation, or Venn diagrams
Example: proving DeMorgan’s theorem using truth table

## Slide 18: Venn Diagrams
Using truth tables to verify theorems and properties can be tedious, and may not be conceptually informative
Venn diagrams are a tool that provides for more intuitive understanding of how expressions may be equivalent
  Graphical illustration of set algebra
  We’re not going to talk about them.

## Slide 19: Equivalent Notations
The following notations are equivalent:
_
X’ same as X
_____
(X + Y)’ same as X + Y

## Slide 20: Other Notation
Using the same symbols for arithmetic and logic can be confusing
We can use the following notation:
  AND ∧, e.g., x1 ∧ x2
  OR ∨, e.g. x1 ∨ x2

## Slide 21: Precedence of Operations
In the absence of parentheses, a logic expression is evaluated in the following order:
  NOT
  AND
  OR

## Slide 22: Computers and Electricity
Gate
A device that performs a basic operation on electrical signals
Circuits
Gates combined to perform more complicated tasks

## Slide 23: Gates
Six types of gates
  NOT
  AND
  OR
  XOR
  NAND
  NOR

## Slide 24: NOT Gate
A NOT gate accepts one input signal (0 or 1) and returns the opposite signal as output

## Slide 25: AND Gate
An AND gate accepts two input signals
If both are 1, the output is 1; otherwise, the output is 0

## Slide 26: OR Gate
An OR gate accepts two input signals
If both are 0, the output is 0; otherwise, the output is 1

## Slide 27: XOR Gate
An XOR gate accepts two input signals
If both are the same, the output is 0; otherwise,
the output is 1

## Slide 28: XOR Gate
Note the difference between the XOR gate and the OR gate; they differ only in one input situation
When both input signals are 1, the OR gate produces a 1 and the XOR produces a 0
XOR is called the exclusive OR
OR is the inclusive OR

## Slide 29: NAND Gate
The NAND gate accepts two input signals
If both are 1, the output is 0; otherwise, the output is 1

## Slide 30: NOR Gate
The NOR gate accepts two input signals
If both are 0, the output is 1; otherwise, the output is 0

## Slide 31: Gates with More Inputs
Gates can be designed to accept three or more input values
A three-input AND gate, for example, produces an output of 1 only if all input values are 1

## Slide 32: Constructing Gates
Gates are constructed with transistors
(Transistor count: http://en.wikipedia.org/wiki/Transistor_count)
  A device that acts either as a wire that conducts electricity or as a resistor that blocks the flow of electricity, depending on the voltage level of an input signal
The easiest gates to create are the NOT, NAND, and NOR gates
You will learn more about this in your digital systems course

## Slide 33: Circuits
Combinational circuit
  The input values explicitly determine the output
Sequential circuit
  The output is a function of the input values and the existing state of the circuit
  We describe the circuit operations using
    Boolean expressions
    Logic diagrams
    Truth tables

## Slide 34: Combinational Circuits
Gates are combined into circuits by using the output of one gate as the input for another

## Slide 35: Combinational Circuits
Three inputs require eight rows to describe all possible input combinations
This circuit is described by the Boolean expression (AB + AC)

## Slide 36: Combinational Circuits
Consider the following Boolean expression A(B + C)
Does this truth table look familiar?
Compare it with previous table…

## Slide 37: Combinational Circuits
Circuit equivalence
Two circuits that produce the same output for identical input
Boolean algebra allows us to apply provable mathematical principles to help design circuits
A(B + C) = AB + AC (distributive law) so circuits must be equivalent
A(B+C)
AB+AC

## Slide 38: Adders
At the digital logic level, addition is performed in binary
Addition operations are carried out by special circuits called, appropriately, adders

## Slide 39: Adders
The result of adding two binary digits could produce a carry value
Recall that 1 + 1 = 10 in base two
Half adder
A circuit that computes the sum of two bits and produces the correct carry bit
Truth table

## Slide 40: Adders
Circuit diagram representing a half adder
Boolean expressions
sum = A  B
carry = AB

## Slide 41: Adders
Full adder
A circuit that takes the carry-in value into account

## Slide 42: Circuits as Memory
Digital circuits can be used to store information
These circuits form a sequential circuit, because the output of the circuit is also used as input to the circuit

## Slide 43: Circuits as Memory
An S-R latch stores a single binary digit (1 or 0)
The output of one gate is used as an input to the other gate

## Slide 44: Circuits as Memory
The design of this circuit guarantees that the two outputs X and Y are always complements of each other
The value of X is considered to be the current state of the circuit
  If X is 1, the circuit is storing a 1
  If X is 0, the circuit is storing a 0

## Slide 45: Circuits as Memory
S | R | X | Y
0 | 0 | Not allowed (forbidden state) | 
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | No change in the output | 
S-R latch truth table

## Slide 46: Integrated Circuits
Integrated circuit (also called a chip)
A piece of silicon on which multiple gates have been embedded
  Silicon pieces are mounted on a plastic or ceramic package with pins along the edges
  Pins can be soldered onto circuit boards or inserted into appropriate sockets

## Slide 47: Integrated Circuits
Integrated circuits (IC) are classified by the number of gates contained in them

## Slide 48: Integrated Circuits
Example SSI chip containing independent NAND gates

## Slide 49: CPU Chips
The most important integrated circuit in any computer is the Central Processing Unit, or CPU
Each CPU chip has a large number of pins through which essentially all communication in a computer system occurs
We will look at the CPU in more detail soon